Network of Pinsky-Rinzel Two-Chamber Neurons

Program: prnnet

Source: prnnet.c

Build script: bld_prnnet

Compiler: gcc

Operating System: Linux

Obsolete, will be updated

Command line

prnnet [{<switch> [<value>]}. .]

| switch | value or format | unit | default | Other nominal values |  |
| --- | --- | --- | --- | --- | --- |
| -nn | integer |  | 10 |  | Number of neurons. |
| -pr | none |  |  |  | Simulate Pinsky-Rinzel single neuron. (see below). No yet implemented. |
| -ef | (see below) |  |  |  | Applied electric field. |
| -nr | none |  |  |  | No resistive lattice. |
| -area | float | cm2 | 6 ×10-6 |  | Membrane surface area. |
| -ap | float, ≤ 1.0 |  | 0.5 |  | Area proportion for soma |
| -gc | float | mS/cm2 | 2.1 | 1.5-2.1 | Dendrite-to-soma conductance. |
| -gnmda | float | mS/cm2 | 0.005 | 0.0 | NMDA conductance. |
| -gampa | float | mS/cm2 | 0.025 | 0.0 | AMPA conductance. |
| -vl | float | mV | 0.0 | 0.1 | Leakage potential |
| -isoma | float | μA/cm2 | 0.0 |  | Steady injected current at soma |
| -idend | float | μA/cm2 | 0.0 | 0.7 | Steady injected current at dendrite |
| -ko | float | mM | 3.50 | 8.50 | Extracellular [K+] (see below). |
| -ca | float | mM | 0.2 |  | Intracellular [Ca++] . |
| -snmda | float |  | 0.6 | 0.3 | Initial value for NMDA synaptic weight |
| -wampa | float |  | 0.5 | 0.2 | Initial value for AMPA synaptic weight |
| -vsoma | float | mV | -4.6 | -4.5±0.4 | Initial Vm for soma |
| -vdend | float | mV | -4.5 | -4.5±0.4 | Initial Vm for dendrite |
| -rand | vs,vd,gc | 5% max |  |  | Randomize one or more of vs, vd and gc.. |
| -dur | float | seconds | 12.5 |  | Duration of run (not working) |
| -ip | (see below) |  |  |  | Injected current pulses. |
| -p | (see below) |  |  |  | Analyze spike propagation. |
| -o | (see below) |  |  |  | Write output to these files. |
| -dir | text string |  |  |  | Create and write to output file directory. |
| -nfs | none |  |  |  | No file suffix. |
| -fts |  |  |  |  | Add timestamp to file name |
| -fn |  |  |  |  | Add note to file name |
| -log | none |  |  |  | Write messages to file. |
| -trace | none |  |  |  | Log intermediate results. |
| -help |  |  |  |  | or –h. Usage display,. |

-pr

Reproduce Pinsky-Rinzel single neuron model

This option is equivalent to the command:

./prnnet –nn 1 –nr –gnmda 0 –gampa 0 –ko 8.5 –idend 0.7

which reproduces the Pinsky-Rinzel model (1994). It has no resistive grids, no synaptic currents, no injected current pulses and no applied fields. As long as NMDA and AMPA conductances are zero, the synaptic potential will has no effect. A steady current of 0.7 μA/cm2 is injected at the dendrite.

e.g. Simulate the Pinsky-Rinzel model to compute somatic and dendritic potentials, and calcium concentration:

./prnnet –pr –o vs,vd,ca

-p <time1>:<spike1>,<time2>:<spike2>. . .

Analyze spike propagation

This option tracks one or more spikes that originate from the neuron that receives the current injections, as specified by a spike number after a certain time. Each pair of parameters specifies a time when the program starts count the spikes at the first neuron, where current would be injected. The program can track a maximum of 128 spikes.

|  |  |  | default |  |
| --- | --- | --- | --- | --- |
| time<n> | float double | seconds | none | Time after which spike is counted at the initiating neuron. |
| spike<n> | integer |  | none | The occurrence count of a spike whose propagation is to be tracked. |

e.g. Track the first, fifth and twentieth spike after onset of electric field. Also track the fourth spike after the eighth second.

./prnnet –nn 10 –ef 5,300 –p 5:5,5:10,5:20,8:4 –o vs,vd

-ip <neurons>,<chamber>,<magnitude>,<duration>,<onset times>

where	<neurons> := all | <neuron> | <neuronA>-<neuronB>

where	<onset_time> := <time1>:<time2>:<time3>. . .

Injected current pulses

One or more pulses of current are injected at the This option specifies the magnitude of the injected current pulse and its onset times. If this options is not specified, no current is injected.

|  |  |  | default |  |
| --- | --- | --- | --- | --- |
| chamber | s ¦ d |  | none | S for soma d for dendrite. |
| magnitude | float double | μA/cm2 | none |  |
| time<n> | float double | seconds | none | Maximum of 64 onset times. |

e.g. ./prnnet –nn 2 –ip 5,2.0;5.0:8.0 –o vs

-ef <time>,<initial>:<increment>:<final>

Electric field pulses

|  |  |  | default |  |
| --- | --- | --- | --- | --- |
| time | float double | seconds | none | Field onset time |
| initial | float double | mV/cm | none | Initial field value |
| increment |  | mV/cm | one field | Incremental value |
| final |  | mV/cm | one field | Final field value |

e.g. ./prnnet –nn 10 –ef 5,300,0.50,500 –o vs,vd

-o <output type>

Write time series output

The first line is a description that starts with the character ‘#’ (it is ignored by gnuplot). Except for the sp option, the spike output file, all files has the time in seconds listed in the first column; the other columns are relevant values for neurons 1 to n. The spike output file has  the spike number listed in the first column and spike onset times for neurons 1 to n in other columns. See the output file section the name of these output files.

| vs | Somatic transmembrane potential |
| --- | --- |
| vd | Dendritic transmembrane potential |
| is | Somatic transmembrane current |
| id | Dendritic transmembrane current |
| ca | Intracellular calcium concentration at the dendritic chamber. |
| ii | Intracellular current from dendrite to soma. |
| vo | Extracellular potential different between the dendrite and the soma. |
| ix | Synaptic current from the soma of one neuron to dendrite the connect neuron. In this mode, it is the sum of NMDA and AMPA current. |
|  | (all variables) |
| ef | Applied electrical field. (?) |
| sp | Time of spike for each neuron. |

e.g.. Write time-series output for membrane potential of soma and dendrite, calcium concentration and synaptic current; also write spike occurrence:

./prnnet –nn 10 –ef 5,300,0.50,500 –o vs,vd,ca,ix,sp

Output files

| file name | turns on by |  |
| --- | --- | --- |
| pr_spike<efield><timestamp>.txt | -o sp | (future) |
| pr_vsoma<efield><timestamp>.txt | -o vs |  |
| pr_vdend<efield><timestamp>.txt | -o vd |  |
| pr_isoma<efield><timestamp>.txt | -o is |  |
| pr_idend<efield><timestamp>.txt | -o id |  |
| pr_conca<efield><timestamp>.txt | -o ca |  |
| pr_isynp<efield><timestamp>.txt | -o ix | Synaptic current |
| pr_id2si<efield><timestamp>.txt | -o ii | Internal dendrite to soma current |
| pr_vd2so<efield><timestamp>.txt | -o vo | External dendrite-soma potential |
| pr_field<efield><timestamp>.txt | -o ef |  |
| pr_sprop<efield><timestamp>.txt | -p .. | Spike propagation. |
| pr_trace<efield><timestamp>.txt | -trace | Intermediate data log such as matrices. |
| Pr_mslog<efield><timestamp>.txt | -log | Message log |
| pr_param<efield><timestamp>.txt | always | Simulation parameters |

| efield | [-¦n]nnnnnnn | 8 digits in mV/cm. The right-most character is either the most significant digit or a negative sign. |
| --- | --- | --- |
| timestamp | YYMMDDHHMMSS | All digits. Specifies year, month, day of month, hour, minute and second. |

Parameter Consistency

Duration –

Onset times must be less than duration.

Pinsky-Rinzel Model

Parameters:

|  |  | PRNeuron01.cpp (gc11.cpp) | prnnet.c | PRNeuron.c (PR_Rev2.cpp) | ODE | Pinksy-Rinzel |
| --- | --- | --- | --- | --- | --- | --- |
| Area |  | 0.000006 | 0.000006 |  |  |  |
| P |  | 0.5 | 0.5 |  | 0.5 |  |
| Cm |  | 3.0 | 3.0 |  | 3.0 | 3.00 |
| K-out |  |  |  |  |  |  |
| gc |  | 2.1 | 2.1 |  | 2.1 | 2.10 |
| gL |  | 0.0 | 0.1 |  | 0.0 | 0.10 |
| gNa |  | 30.0 | 30.0 |  | 30.0 | 30.00 |
| gKDR |  | 15.0 | 15.0 |  | 15.0 | 15.00 |
| gCa |  | 10.0 | 10.0 |  | 10.0 | 10.00 |
| gKAHP |  | 0.8 | 0.8 |  | 0.8 |  |
| gKCa |  | 15.0 | 15.0 |  | 15.0 |  |
| gNMDA |  |  | 0.0 |  |  |  |
| gAMPA |  |  | 0.0 |  |  |  |
| sNMDA |  | 0.6 | 0.6 |  |  |  |
| sAMPA |  | 0.5 | 0.5 |  |  |  |
| vNa |  | 120.0 | 120.0 |  | 120.0 | 120.00 |
| vCa |  | 140.0 | 140.0 |  | 140.0 | 140.00 |
| vK* |  | -15.0 -38.56 | -15.0 -38.56 |  | -15.0 | -15.00 |
| vL |  | 0.0 | 0.0 |  | 0.0 | 0.0 |
| vsyn |  | 60.0 | 60.0 |  | 60.0 |  |
| vsoma | mV | -4.6 | -4.6 |  | -4.6 |  |
| vdend |  | -4.5 | -4.5 |  | -4.5 |  |
| isoma |  | 0.0 | 0.0 | 2.0 |  | -0.50 |
| idend |  | 0.0 | 0.0 | 0.0 | 0.7 | 0.00 |

Variables - Initial Values

|  |  | PRNeuron01.cpp (gc11.cpp) | prnnet.c | PRNeuron.c (PR_Rev2.cpp) | ODE | Pinksy-Rinzel |
| --- | --- | --- | --- | --- | --- | --- |
| h |  |  |  |  |  |  |
| n |  |  |  |  |  |  |
| s |  |  |  |  |  |  |
| c |  |  |  |  |  |  |
| q |  |  |  |  |  |  |
| [Ca] |  | 0.2 |  |  |  |  |
| ss - NMDA |  |  |  |  |  |  |
| ws -AMPA |  |  |  |  |  |  |
| vsoma |  | -4.6 | -4.6 | -4.6 | -4.6 |  |
| vdend |  | -4.5 | -4.5 |  | -4.5 |  |

Change

- Removed Fortran-style matrix “physical dimensions” indexing.

- Replaced matrix representation with 2-dimemsional arrays.

- Modified fourth order Runge-Kutta function for matrix, rk4m().

- Added data structures for model parameters.

- Added command line options for selecting simulation parameters.

- Organized output files; output to specified directory.

Problems with gc11.cpp

- derivs() – “S and W synaptic derives” should be V-soma, not V-dendrite.

- derivs() – DYDT for soma and dendrite, divide by p, 1-p?

- rinf – hard-coded vsyn. (minor)

- randomization - hard-coded for 10 neurons

- spiking – hard-coded for <5 neurons

Findings

- Resistive lattice causes slight difference between neurons (through vdsout term).

Future

- Improve simulation loop – add propagation and multiple current pulses.

- .

Questions

References